## Slide 1: Mobile Device and Cloud Server based Intelligent Health Monitoring Systems
Sub-track in audio - visual processing
NAME: ZHAO Ding
SID: 52208367
Supervisor: Prof YAN, Hong
Assessor: Dr CHAN, Rosa H M

## Slide 2: Objectives
Develop an Android App:
To display the user’s talking speech pitch in the run time. To generate the pitch contour and pitch range analysis.
To measure the user’s heart rate using the built-in camera.
To recognize the user’s emotion status based on captured facial image and recorded daily for long-term monitoring.

## Slide 3: Motivations
Fast life pace. Work stress. Inconvenient to visit hospital.
Chronic diseases and mental health problems.
Essential to keep a record of daily emotion status.

## Slide 4: Motivations
Smartphones:
indispensible part of modern life.
Possible for health condition monitoring.

## Slide 5: Work Done
Voice Disorder Checker
Heart Rate Monitor
Emotion Tracker

## Slide 6: Work Done
Voice Disorder Checker
Heart Rate Monitor
Emotion Tracker

## Slide 7: Voice Disorder Checker
Background
Clinicians & subjective rating.
Time-consuming.
Special instrument or complex software. [1]

## Slide 8: Voice Disorder Checker
Record, sample and digitalize
Pitch calculation and display
sampling rate = 44100 Hz, encoding format = PCM 16 bit
Feature extraction
Timeframe: 46ms
Pitch detection algorithms
Alert for abnormal feature

## Slide 9: Voice Disorder Checker
Pitch Detection Algorithms
Direct Fast Fourier Transform
Harmonic Product Spectrum [2]
Cepstrum Analysis [3]

## Slide 10: Voice Disorder Checker
Cepstrum Analysis
Cepstrum of particular speech segment
High-Key voice
Low-Key voice
Pitch contour over time
(do re mi fa so la si do)

## Slide 11: Voice Disorder Checker
Checking Results:[5]
Abnormal Features | Related Voice Disorders
Unmatched pitch contour shape | Dysprosody
Reduced pitch range | Vocal fold nodule, Vocal Hemorrhage
Excessively high or low pitch | Bogart–Bacall syndrome, Muscle Tension Dysphonia

## Slide 12: Work Done
Voice Disorder Checker
Heart Rate Monitor
Emotion Tracker

## Slide 13: Heart Rate Monitor
Background

## Slide 14: Heart Rate Monitor
Video record
Heartbeat ++
Red pixel value > Avg value
Heart Rate deduction
Average red pixel intensity calculation
Use PreviewCallback to grab the latest image
Collect data in 10 sec chunk

## Slide 15: Heart Rate Monitor
Image color intensity calculation
YUV420SP != ARGB
Y = luminance
U and V = chrominance

## Slide 16: Work Done
Voice Disorder Checker
Heart Rate Monitor
Emotion Tracker

## Slide 17: Emotion Tracker
Background
Static Approach
  FisherFace Model
  EigenFace Model [6]
  Active Appearance Model [7]
Dynamic Approach
  FACS intensity tracking [8]

## Slide 18: Emotion Tracker
Background
Static Approach
  FisherFace Model
  EigenFace Model [6]
  Active Appearance Model [7]
Dynamic Approach
  FACS intensity tracking [8]

## Slide 19: Emotion Tracker
Facial image capture
Feed to EigenFace model trained
Classification result recorded
Long term monitoring report
Model trained from JAFFE database

## Slide 20: Emotion Tracker
EigenFace model
Principal Component Analysis
Training images from JAFFE database:
Store training data in xml file
Average Eigen Image
Training images eigenfaces

## Slide 21: Emotion Tracker
EigenFace model
Load training data and test image
Run the find nearest neighbor algorithm

## Slide 22: Conclusions
VoiceDisorderChecker:
Real-time speech pitch tracking.
HeartRateMonitor:
Heartbeat counting. Red pixel intensity variation of index fingertip image, representative of blood pulse rhythm.
EmotionTracker:
Static facial image expression recognition.

## Slide 23: Work to be Done
Refine the pitch detection algorithm.
Evaluate the performance of EmotionTracker using figherface model.
More emotion categories when training eigenface model
Better design for App user interface
Release as beta version
Deploy the App to Google Cloud Platform

## Slide 24: References
[1] Koichi OMORI, “Diagnosis of Voice Disorders,” JMAJ, Vol. 54, No. 4, pp. 248–253, 2011.
[2] TCH DETECTION METHODS REVIEW [Online]. Available: http://ccrma.stanford.edu/~pdelac/154/m154paper.htm
[3] A. Michael Noll, “Cepstrum Pitch Determination,” Journal of the Acoustical Society of America, Vol. 41, No. 2, (February 1967), pp. 293-309.
[4] Alan V. Oppenheim and Ronald W. Schafer, Discrete-Time Signal Processing, Prentice Hall, 2009.
[5] Deirdre D. Michael. (2012, Dec 1). Types of Voice Disorders. [Online]. Available: http://www.lionsvoiceclinic.umn.edu/page3b.htm

## Slide 25: References
[6] Gender Classification with OpenCV. [Online]. Available at http://docs.opencv.org/trunk/modules/contrib/doc/facerec/tutorial/facerec_gender_classification.html#fisherfaces-for-gender-classification
[7] Timothy F. Cootes, Gareth J. Edwards, and Christopher J. Taylor. “Active Appearance Models.” IEEE TRANSACTIONS ON PATTERN ANALYSIS AND MACHINE INTELLIGENCE, VOL. 23, NO. 6, JUNE 2001.
[8] Maja Pantic, Student Member, IEEE, and Leon J.M. Rothkrantz. “Automatic Analysis of Facial Expressions: The State of the Art.” IEEE TRANSACTIONS ON PATTERN ANALYSIS AND MACHINE INTELLIGENCE, VOL. 22, NO. 12, DECEMBER 2000.

## Slide 26: Q & A